Measuring Planck’s Constant by Observation of the Photoelectric Effect

---
Theory
- Photoelectric Effect: Electrons can be ejected from a metal irradiated by electromagnetic radiation.
- Electrons bound to metal by binding energy
- Increased frequency: increased electron kinetic energy

---
Theory
- Albert Einstein: light is made of particles called photons
- Photons carry energy proportional to the frequency of the light
- Increased intensity: more photons, but not more energy in each photon

---
Experiment
- Irradiate a metal cathode with light of a known frequency and measure the produced photocurrent
- Vary the voltage between cathode and anode to find the stopping voltage.
- Repeat for several wavelengths of light.
- By energy conservation, we have:
  |Vs| = (hc/e) (1/λ) + Φ/e

---
Experimental Setup

---
Current Vs. Voltage Graph

---
Determination of Stopping Potential
- Used a statistical technique.
- Fit a line to the first thirty data points.
- Calculated the standard deviation of these points from the fitted line.
- Found a critical line, which was the best fit line shifted up three standard deviations.
- Defined the stopping potential to be the voltage that corresponded to the first data point for which all subsequent points lie above the critical line.

---
Results

---
Results
- Best fit line: |Vs| = (3.1 × 10−7 ± 0.8 × 10−7 Vm) (1/λ) + (−0.2 ± 0.2 V)
- This implies values of:
  h = 1.6 × 10−34 ± 0.4 × 10−34 Js
  Φ = −0.2 ± 0.2 eV
- These results do not agree with the accepted values of these quantities.

---
Errors in Results
- Noise in the current measurements.
- Excessive photoemission from the anode.
- Filters having an unknown effect on the incident light.