Measuring Planck’s Constant by Observation of the Photoelectric Effect

---
Theory
- Photoelectric Effect: Electrons can be ejected from a metal irradiated by electromagnetic radiation.
- The kinetic energy of the ejected electrons was found to increase with the frequency of the radiation, not the intensity.
- Albert Einstein explained this by hypothesizing that light does not travel as a wave but rather as particles.

---
Theory
- Einstein hypothesized that the photons carried energy proportional to the frequency of the light, with Planck’s constant as the proportionality constant.
- Increased intensity: more photons, but not more energy in each photon

---
Experiment
- Irradiate a metal cathode, pick up ejected electrons on an anode and measure the produced current.
- Vary the voltage between cathode and anode to find the stopping voltage.
- Measure stopping voltage for several wavelengths of light.
- Then by energy conservation, we have:
  |Vs| = (hc/e) (1/λ) + Φ/e

---
Current Vs. Voltage Graph

---
Determination of Stopping Potential
- Used a statistical technique.
- Fit a line to the first thirty data points.
- Calculated the standard deviation of these points from the fitted line.
- Found a critical line, which was the best fit line shifted up three standard deviations.
- Defined the stopping potential to be the voltage that corresponded to the first data point for which all subsequent points lie above the critical line.

---
Results

---
Results
- Best fit line: |Vs| = (3.1 × 10−7 ± 0.8 × 10−7 Vm) (1/λ) + (−0.2 ± 0.2 V)
- This implies values of:
  h = 1.6 × 10−34 ± 0.4 × 10−34 Js
  Φ = −0.2 ± 0.2 eV
- These results do not agree with the accepted values of these quantities.

---
Errors in Results
- Noise in the current measurements.
- Filters having an unknown effect on the incident light.